## Slide 1: Embedded and Real-Time Systems Spring 2021
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology

## Slide 2: Grading
Final Exam: 40%
Midterm Exam: 30%
Homework and Projects: 20%
Attendance and Activities: 10%
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran

## Slide 3: Textbook
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Giorgio Buttazzo

## Slide 4: Copyright Notice
This lecture is adopted from
IN4343 Real-Time Systems Course 2018 – 2019, Mitra Nasri,
Delft University of Technology
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran

## Slide 5
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Introduction and taxonomy

## Slide 6: What is an embedded system?
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Embedded system:
A computer system that is “embedded” in a physical/mechanical system and usually performs a set of specific functions.
It often interacts with its environment.

## Slide 7: What is a real-time system?
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Real-time system
A system whose correctness depends not only on the correctness of logical results (e.g., decisions), but also on the time at which the results are produced.
If the system does not react “on time”, something can go wrong!

## Slide 8: Embedded vs. real-time systems
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Real-time, but not embedded
Stock trading system
Skype
Video streaming/processing
Real-time embedded
Nuclear reactor control
Flight control
Mobile phone
Drone
Embedded, but not real-time
Home temperature control
Washing machine, refrigerator, etc.
Blood pressure meter
Embedded systems
Real-Time systems

## Slide 9: Characteristics of real-time systems
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Event-driven, reactive
High cost of failure
timeliness
Collision
Too late
time
Too early
Example: airbag system
Airbag is fully open
Response time

## Slide 10: Classes of real-time systems
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Hard real-time
  systems where it is absolutely imperative that responses occur within the required deadline.
Safety-critical systems
(wrong/late decisions endanger human life or the environment’s safety)

## Slide 11: Classes of real-time systems
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Hard real-time
  systems where it is absolutely imperative that responses occur within the required deadline.
Business-critical systems
(wrong/late decisions lead to financial losses)
Source: Oce industrial printers
https://vimeo.com/119897713

## Slide 12: Classes of real-time systems
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Soft real-time
  systems where deadlines are important but which will still function correctly if deadlines are occasionally missed.
wrong/late decisions reduce user
satisfaction or quality of service

## Slide 13: Classes of real-time systems
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Firm real-time
  systems which are soft real-time but in which there is no benefit from late delivery of service.
Virtual reality
Video streaming
Voice over IP

## Slide 14: An example: a self-balancing device
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Inverted pendulum:
http://www.st.ewi.tudelft.nl/mitra/teaching/rts/2019/files/inverted_pendulum.mp4
https://www.youtube.com/watch?v=a4c7AwHFkT8
Timeliness is important for stability
What type of real-time systems is it?
How about this one?

## Slide 15: A Closer Look
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
The control task is activated
time
A/D reads the sample data
Controller task applies the control law
D/A writes the output
control-law computation
A/D
A/D
D/A
actuator
r
k
y
k
y(t)
sensor plant
How is it implemented?
u(t)
u
k
reference input r(t)
The system
being controlled
Outside effects
(gravity, perturbations, …)
u(t)
r(t)
y(t)
A periodic controller
The control task is activated again
While(true)
{
Read input;
Compute control command;
Write output;
Sleep (until the next sampling period);
}

## Slide 16: How is it implemented?
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
The control task is activated
time
Read input
Compute the control command
Write output
While(true)
{
Read input;
Compute control command;
Write output;
Sleep (until the next period);
}
Actuators
Sensors
Code (compiled for the micro-processor)
Microprocessor
physical/mechanical/electrical part
Onboard
sensors
Looks predictable, right?
What if the system has more tasks?

## Slide 17: A more complicated system
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Adaptive cruise control (ACC)
https://www.youtube.com/watch?v=r8G0n5LeJo0

## Slide 18: Adaptive cruise control
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Multiple sensors
Multiple tasks
Various periods of activation
Shared data
Event-based activation

## Slide 19: Multi-task system
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Actuators
Sensors
Operating system (or libraries)
Scheduler
software
hardware
time-sensitive applications App. 1 App. 2 App. 3
Cyber part

## Slide 20: In the course, you will learn What influences the response time of a system (or its tasks) How one can evaluate/analyze the response time How one can make/design a time-predictable system
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran

## Slide 21: Taxonomy of real-time systems
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran

## Slide 22: Definitions
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Task
  A code that implements one of the system functionalities
  It can have multiple inputs and outputs
  It can be activated by events (e.g., user command or a network interrupt) or by time (e.g., by periodic timer interrupt)
Tasks usually
  Share data
  Communicate with each other
  Perform I/O operations
  …

## Slide 23: Definitions
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Job (instance of a task)
  A job is an instance of a task that has arrived to the system (e.g., by the activation of a timer interrupt)
Task 2
Task 1
First job
𝐽1,1
𝐽2,1
First job
…
…
Second job
𝐽1,2
10
0
Third job
𝐽1,3
20
Second job
𝐽2,2
4
0
Third job
𝐽2,3
13
Fourth job
𝐽2,4
20

## Slide 24: Workload characterization
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Activation pattern of the tasks
  Periodic
    Single rate (all tasks have the same period)
    Multi rate (tasks have different periods)
  Aperiodic
    Bounded arrival time (sporadic)
    Unbounded arrival time (event-based activation)

## Slide 25: Taxonomy
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Periodic
Each task (or group of tasks) executes repeatedly with a particular period
It allows static analysis techniques to be used
It is widely used in real systems
Task 2
Task 1
Release time
15
0
30
0
10
20
30

## Slide 26: Taxonomy
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Task 2
Task 1
Release time
15
0
30
0
10
20
30
Types of periodic tasks
Single rate
  One period in the system
  Simple but inflexible
  Used in implementing a lot of sensor networks
Multi rate
  Multiple periods

## Slide 27: Taxonomy
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Aperiodic
Aperiodic tasks are activated by events
The workload is dynamic (cannot be predicted)
Task 1
deadline
15
0
55

## Slide 28: Taxonomy
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Event-based tasks
There is no lower-bound or upper-bound on the activation time of the next job of such task
Task 1
Example: engine control task in the car
The activation time between two jobs is proportional to the speed of the engine, i.e., the faster you drive, the higher is the frequency of job releases

## Slide 29: Taxonomy
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Analyzing aperiodic tasks is challenging
Since it is hard to predict the future workload, it is hard to analyze the system to find the worst-case response time of the tasks
With unbounded arrival times, it is impossible to guarantee the timeliness of a resource-constrained system
Task 1
0
10 16
Impossible to meet all deadlines

## Slide 30: Characterization of the deadline
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Type of deadlines
  Hard
  Soft
  Firm
Relation between deadline and period
  Implicit deadline
  Constrained deadline
  Arbitrary deadline

## Slide 31: Criticality / timeliness
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
soft
firm
hard
criticality
Utility functions

## Slide 32: Taxonomy
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Relation between deadline and period
Implicit deadline: deadline is equal to period
Constrained deadline: deadline is smaller than or equal to period
Arbitrary deadline: deadline can be smaller, equal, or larger than period

## Slide 33: Execution Model
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Preemptive execution
  The execution of a task may be forcefully preempted (stopped) by the system (scheduler)
Non-preemptive execution
  A task does not leave the processor (or resource) until it
completes or suspend itself

## Slide 34: Taxonomy
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Static
Task arrival times can be predicted
Static (compile-time) analysis possible
  task length is known
  WCET
Allows good resource usage (high CPU utilization)

## Slide 35: The “Window of Scarcity”
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Resources may be categorized as:
Abundant
  Virtually any system design methodology can be used to realize the timing requirements of the application
Insufficient
  The application is ahead of the technology curve; no design methodology can be used to realize the timing requirements
Sufficient, but scarce
  It is possible to realize the timing requirements of the application, but careful resource allocation is required

## Slide 36: Course focus
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Designing predictable RTSs
  fast != real-time
We will focus on
  Proving vs. testing
  Hard vs. soft real-time
  Worst-case response time vs. best effort
Study various scheduling policies