## Slide 1: Embedded and Real-Time Systems Spring 2021
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 3

## Slide 2: Copyright Notice
This lecture is adopted from
IN4343 Real-Time Systems Course 2018 – 2019, Mitra Nasri,
Delft University of Technology
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Online Scheduling
Buttazzo’s book, chapter 2

## Slide 3: Agenda
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Modeling real-time systems
Real-time tasks: formal definitions
Online scheduling
If you want to remember something
from the course, it should be this section.
Tip: to secure a good grade, learn this section very well.

## Slide 4: Definitions: Schedule
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Schedule is a particular assignment of tasks to the processor(s) and time intervals. It determines the task execution sequence.
𝑘 = 0
𝑘 > 0
in [𝑡𝑖 , 𝑡𝑖+1) the processor is IDLE
in [𝑡𝑖 , 𝑡𝑖+1) the processor is executing task 𝜏𝑘
Formally, given a task set 𝜏 ={𝜏1, 𝜏2, …, 𝜏𝑛}, a schedule is a function 𝜎: ℝ+ →ℕ that associates an integer 𝑘 to each interval of time [𝑡𝑖 , 𝑡𝑖+1) with the following meaning:

## Slide 5: Example: Schedule
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran

## Slide 6: Preemptive scheduling
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran

## Slide 7: Example: task states in preemptive scheduling
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran

## Slide 8: Definitions
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
A schedule 𝜎 is said to be feasible if and only if it satisfies all given requirements, for example, “no deadline is missed in 𝜎”.
A task set 𝜏 is said to be feasible,
If and only if there exists a feasible schedule for 𝜏.
A task set 𝜏 is said to be schedulable with an algorithm 𝐴,
if and only if 𝑨 generates a feasible schedule for 𝜏.

## Slide 9: Online scheduling
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Recall:
dispatching
Task completion
Preemption or suspension
Scheduling alg.
pending queue
Online scheduler
Ready queue
Task activation (release)
CPU
What scheduling policies (or algorithms) do you know?

## Slide 10: Some well-known scheduling algorithms
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
First-in-first-out scheduling (FIFO)
= First-come-first-serve (FCFS)
Round robin
Shortest-job first
Earliest deadline first (EDF)
Fixed-priority scheduling (FP)

## Slide 11: Example: FIFO
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
𝜏1
𝜏2
10
2
5
𝜏𝑖 | 𝐶𝑖 | a𝑖 | 𝑑𝑖
𝜏1 | 8 | 5 | 14
𝜏2 | 3 | 10 | 14
𝜏3 | 4 | 2 | 17
14
14
17
𝜏3
What would be the schedule?

## Slide 12: Example: FIFO
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
𝜏𝑖 | 𝐶𝑖 | a𝑖 | 𝑑𝑖
𝜏1 | 8 | 5 | 14
𝜏2 | 3 | 10 | 14
𝜏3 | 4 | 2 | 17
17
3
miss
𝜏1
𝜏
2
10
2
5 6
14
14
17
𝜏3
Let’s see how this schedule is produced

## Slide 13: Example: FIFO
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
2
𝜏𝑖 | 𝐶𝑖 | a𝑖 | 𝑑𝑖
𝜏1 | 8 | 5 | 14
𝜏2 | 3 | 10 | 14
𝜏3 | 4 | 2 | 17
dispatching
Task completion
Preemption or suspension
Scheduling alg.
pending queue
Online scheduler
Ready queue
Task activation (release)
CPU
At time 2:
𝜏3
17
𝜏1
𝜏2
𝜏3

## Slide 14: Example: FIFO
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
2
𝜏𝑖 | 𝐶𝑖 | a𝑖 | 𝑑𝑖
𝜏1 | 8 | 5 | 14
𝜏2 | 3 | 10 | 14
𝜏3 | 4 | 2 | 17
dispatching
Task completion
Preemption or suspension
Scheduling alg.
pending queue
Online scheduler
Ready queue
Task activation (release)
CPU
from 2+𝜖 until 5:
𝜏3
17
𝜏1
𝜏2
𝜏3
What is this 𝝐 for?
Answer: context switch and the runtime of the scheduler

## Slide 15: Example: FIFO
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
𝜏1
𝜏2
2
5
𝜏𝑖 | 𝐶𝑖 | a𝑖 | 𝑑𝑖
𝜏1 | 8 | 5 | 14
𝜏2 | 3 | 10 | 14
𝜏3 | 4 | 2 | 17
14
dispatching
Task completion
Preemption or suspension
Scheduling alg.
pending queue
Online scheduler
Ready queue
Task activation (release)
CPU
From 5+𝜖 until 6:
𝜏1
𝜏3
17
𝜏3

## Slide 16: Example: FIFO
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
𝜏1
𝜏2
10
2
𝜏𝑖 | 𝐶𝑖 | a𝑖 | 𝑑𝑖
𝜏1 | 8 | 5 | 14
𝜏2 | 3 | 10 | 14
𝜏3 | 4 | 2 | 17
14
14
5 6
dispatching
Task completion
Preemption or suspension
Scheduling alg.
pending queue
Online scheduler
Ready queue
Task activation (release)
CPU
𝜏2
𝜏1
From 10+𝜖 until 14:
17
𝜏3

## Slide 17: Example: FIFO
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
17
3
miss
𝜏1
𝜏
2
10
2
𝜏𝑖 | 𝐶𝑖 | a𝑖 | 𝑑𝑖
𝜏1 | 8 | 5 | 14
𝜏2 | 3 | 10 | 14
𝜏3 | 4 | 2 | 17
14
14
5 6
dispatching
Task completion
Preemption or suspension
Scheduling alg.
pending queue
Online scheduler
Ready queue
Task activation (release)
CPU
𝜏2
From 14+𝜖 until 17:
17
𝜏3

## Slide 18: Is the task set feasible?
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
16
miss
𝜏1
𝜏2
10
2
5
𝜏𝑖 | 𝐶𝑖 | a𝑖 | 𝑑𝑖
𝜏1 | 8 | 5 | 14
𝜏2 | 3 | 10 | 14
𝜏3 | 4 | 2 | 17
14
14
17
Why?
Because whatever you do, you cannot find a solution without a deadline miss. Try!
In general, this claim needs a proof!
𝜏3

## Slide 19: Is the task set feasible?
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
16
miss
𝜏1
𝜏2
10
2
5
𝜏𝑖 | 𝐶𝑖 | a𝑖 | 𝑑𝑖
𝜏1 | 8 | 5 | 14
𝜏2 | 3 | 10 | 14
𝜏3 | 4 | 2 | 17
14
14
17
𝜏3
3
What would be the maximum number of deadline misses that this task set may have for “any imaginable” scheduling algorithm?

## Slide 20: How?
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
My “just-invented-scheduling-policy-for-fun” (JISPFF) schedules each task 𝜏𝑖 at time 𝑖 × 10
𝜏1
𝜏2
𝜏3
10
2
5
14
14
17
18
10
miss
23
20
miss
34
30
miss

## Slide 21
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
It is easy to mess up!
Never under estimate the power of a BAD scheduling algorithm!

## Slide 22: Quiz
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
What is the response time of Task 1?
9 = 14-5
17
3
10
2
5
14
14
17
6
6
8
Task 1
Task 2
4
Task 3

## Slide 23: Quiz
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
With a FIFO schedule, what is the earliest time at which a task
completes?
Task 1
4
7
5
17
10
15
Task 2
Task 3
𝐶1 = 5
𝐶2 = 10
𝐶3 = 1
Task 1
4
7
5
17
10
15
Task 2
Task 3
𝐶1 = 5
𝐶2 = 10
𝐶3 = 1
19
20
14

## Slide 24: Quiz
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
How many deadline misses in the FIFO schedule?
Task 1
4
7
5
17
10
15
Task 2
Task 3
𝐶1 = 5
𝐶2 = 10
𝐶3 = 1
Task 1
4
7
5
17
10
15
Task 2
Task 3
𝐶1 = 5
𝐶2 = 10
19
2
miss
miss 𝐶3 = 1
20

## Slide 25: Quiz
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
What is the response time of Task 1 in the FIFO schedule?
Task 1
4
7
5
17
10
15
Task 2
Task 3
𝐶1 = 2
𝐶2 = 10
𝐶3 = 1
Task 1
4
7
5
17
10
15
Task 2
Task 3
𝐶1 = 2
𝐶2 = 10
𝐶3 = 1
14
19
Completion time of Task 1
𝑓1 = 19
Response time of Task 1
𝑅1 = 𝑓1 − 𝑎1 = 19 − 5 = 14

## Slide 26: Is this task set feasible?
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Task 1
4
7
5
17
10
15
Task 2
Task 3
𝐶1 = 2
𝐶2 = 10
𝐶3 = 1
Task 1
4
7
5
17
10
Task 2
Task 3
𝐶1 = 2
𝐶2 = 10
𝐶3 = 1
15
Yes! Here is one feasible schedule for it:

## Slide 27
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
In a feasible schedule, which task(s) might be executing at time 14? (Think carefully)
Task 1
4
7
5
17
10
15
Task 2
Task 3
𝐶1 = 2
𝐶2 = 10
𝐶3 = 1
Only Task 2.
If at time 14, any other task than Task 2 is executing, that schedule will not be feasible!
Task 1
4
7
5
17
10
Task 2
Task 3
𝐶1 = 2
𝐶2 = 10
𝐶3 = 1
15

## Slide 28: Summary
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Modeling timing behavior of a task
Understanding the title of the course
Learning about online scheduling
Learning the difference between “feasible” and “schedulable”