## Slide 1: Embedded and Real-Time Systems Spring 2021
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 8

## Slide 2: Copyright Notice
This lecture is adopted from
IN4343 Real-Time Systems Course 2018 – 2019, Mitra Nasri,
Delft University of Technology
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Online scheduling of periodic tasks
Buttazzo’s book, chapter 4

## Slide 3: Agenda
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Scheduling algorithms for periodic real-time systems (chapter 4):
  Processor sharing
  Cyclic scheduling Quiz
  Rate monotonic (RM)
  Deadline monotonic (DM)
  (EDF will be discussed in the next lecture)
RM schedulability tests
  Necessary v.s. sufficient tests
  Liu and Layland’s test [1973]
  Hyperbolic bound [2000]
If you want to pass the course, learn this lecture very well

## Slide 4: Fixed-priority scheduling
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Method
Assign priorities to each task based on its timing constraints
  Rate monotonic
  Deadline monotonic
Verify the feasibility of the schedule using analytical techniques
Execute tasks on a priority-based kernel

## Slide 5: Priority assignment for fixed-priority scheduling
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Example: 𝑇 = 10 ⇒ 𝑟𝑎𝑡𝑒 =1/10
Rate monotonic
Assign priorities monotonically with the activation frequency, a.k.a., rate
(~1 / 𝑇) such that a task with a smaller period gets a higher priority
𝝉𝒊 | 𝑪𝒊 | 𝑻𝒊 | 𝑫𝒊 | 𝑼𝒊
𝝉𝟏 | 1 | 5 | 5 | 0.2
𝝉𝟐 | 10 | 40 | 15 | 0.25
𝝉𝟑 | 1 | 20 | 20 | 0.05
Priority ordering?
P1 < P3 < P2
3
4
3
20
40
0
15
𝝉𝟏
𝝉𝟐
𝝉𝟑

## Slide 6: Priority assignment for fixed-priority scheduling
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
𝝉𝒊 | 𝑪𝒊 | 𝑻𝒊 | 𝑫𝒊 | 𝑼𝒊
𝜏1 | 1 | 5 | 5 | 0.2
𝜏2 | 10 | 40 | 15 | 0.25
𝜏3 | 1 | 20 | 20 | 0.05
Deadline monotonic
Assign priorities monotonically with the relative deadline of the task, (~1 / 𝐷)
such that a task with a smaller relative deadline gets a higher priority
Priority ordering?
P1 < P2 < P3
4
4
2
20
40
0
15
𝝉𝟏
𝝉𝟐
𝝉𝟑

## Slide 7: Is rate-monotonic an optimal scheduling policy (in the sense of feasibility)?
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
𝜏1
𝜏2
9
18
12
6
0
3
4
3
3
4
𝝉𝒊 | 𝑪𝒊 | 𝑻𝒊 | 𝑫𝒊 | 𝑼𝒊
𝜏1 | 3 | 6 | 6 | 0.5
𝜏2 | 4 | 9 | 9 | 0.44
Is this task set feasible? (∀𝒊, 𝑫𝒊 = 𝑻𝒊) Is this task set schedulable by EDF?
Is this task set schedulable by RM?
Yes!
Yes! (the schedule shown here is EDF)

## Slide 8: Is rate-monotonic an optimal scheduling policy (in the sense of feasibility)?
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
𝝉𝒊 | 𝑪𝒊 | 𝑻𝒊 | 𝑫𝒊 | 𝑼𝒊
𝜏1 | 3 | 6 | 6 | 0.5
𝜏2 | 4 | 9 | 9 | 0.44
Is this task set feasible? (∀𝒊, 𝑫𝒊 = 𝑻𝒊) Is this task set schedulable by EDF?
Is this task set schedulable by RM?
Yes!
Yes! (the schedule shown here is EDF)
𝜏1
𝜏2
18
12
0
3
3
3
2
6
3 1 2
Deadline miss 9
No!

## Slide 9
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Fixed-priority scheduling with RM priorities is not an optimal
scheduling policy (in the sense of feasibility)
However, if ∀𝒊, 𝑫𝒊 = 𝑻𝒊 then
the rate monotonic priority assignment is an optimal priority assignment among all other priority assignment methods

## Slide 10: Rate monotonic is optimal
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
RM is optimal among all fixed priority algorithms (if Di = Ti):
If there exists a fixed priority assignment which leads to a feasible schedule for τ, then the RM assignment is feasible for τ
If τ is not schedulable by RM, then is cannot be scheduled by any fixed priority assignment

## Slide 11: Deadline Monotonic is optimal If Di ≤ Ti then the optimal priority assignment is given by Deadline Monotonic (DM)
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran

## Slide 12: EDF optimality
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
EDF is optimal among all algorithms:
If there exists a feasible schedule for τ, then EDF will generates a feasible schedule for τ
If τ is not schedulable by EDF, then is cannot be scheduled by any algorithm

## Slide 13: Optimality
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran

## Slide 14: Agenda
Embedded and Real-Time Systems, Spring 2021, AUT, Tehran, Iran
Scheduling algorithms for periodic real-time systems (chapter 4):
  Processor sharing
  Cyclic scheduling Quiz
  Rate monotonic (RM)
  Deadline monotonic (DM)
  (EDF will be discussed in the next lecture)
RM schedulability tests
  Necessary v.s. sufficient tests
  Liu and Layland’s test [1973]
  Hyperbolic bound [2000]
If you want to pass the course, learn this lecture very well